## Slide 1: Timing beyond the basestation
Tim Frost | ITSF 2018

## Slide 2: Beyond the edge?
Synchronisation beyond the edge
Getting synchronisation beyond the edge
Delay compensation
Measurement
Conclusions
Image: Michal Osmenda
Cliffs of Moher, County Clare, Eire

## Slide 3
Synchronisation beyond the edge

## Slide 4: What’s beyond the edge?
For accurate timing, it’s a new world
Most network synchronisation has focused on maintaining the network itself
5G pushes the timing beyond the edge, out to the customer
There be dragons…
Image: The Flat Earth Society

## Slide 5: Sensor fusion
Combining data from multiple sensors
  Radar
  Lidar
  Ultrasound
  Infra-red
  Camera
  Inertial
Basis for combination is accurate time
Image: innovation-destination.com

## Slide 6: Connected Vehicles
V2X communication
  Vehicle-to-vehicle
  Vehicle-to-infrastructure
  Vehicle-to-pedestrian
Communication of PVT data
  Position
  Velocity
  Time
Image: Qatar Mobility Innovations Center

## Slide 7: Intelligent Transport Systems
Not just sensor fusion…
Not just V2X…
Connected, intelligent systems
Timely data important for good decision making
  Low latency
  Accurate timestamping
Image: Society of Motor Manufacturers and Traders

## Slide 8: Smart Cities
Intelligent Traffic Management
Smart Public Transport
Smart Energy Management
Smart Communications and Information
Security Systems
Waste Management
Crowd Management
Image: Amaresco

## Slide 9
Getting synchronisation beyond the edge

## Slide 10: Getting synchronisation beyond the edge
Surely we’ve always had this?
  I turn on my phone, it automatically synchronises to network time
  My computer does the same thing
NTP is ubiquitous, it’s been around for 30 years, it’s well suited for most networked applications
  Provides millisecond level timing…
What if we could get time to another level of accuracy?
  Microsecond-level timing or better beyond the basestation…
Can we use GNSS?
  Yes, but not always available or visible
Can we use the cellular signal (4G, 5G) itself to deliver time?

## Slide 11: Synchronisation over the air
What if you could synchronise from the cellular signal itself?
Primary and secondary synchronisation signals are used to identify the radio frame
If the radio frames are known to be aligned to the start of each second, (e.g. within 1.5s), then the radio frame position can be used to communicate accurate time
Technique known as “radio interface based synchronisation” or RIBS
Need to compensate for the time-of-flight of the radio frame through the air
eNodeB
Time Sync
(e.g. PTP, GNSS)
Primary, Secondary Synchronisation signals
radio frame
UE

## Slide 12
Delay Compensation

## Slide 13: Timing Advance
Timing advance alters the UE transmission timing to ensure frames line up at the BS
Timing advance is a measure of round trip delay, and can be used to compensate BS sync
UE slot
UE slot
BS slot
At BS
BS slot
BS slot
UE slot
UE slot
BS slot
At BS
BS slot
BS slot
At UE
BS frame
BS frame
UE frame
UE tx time
UE frame
UE frame
UE frame
Guard band
UE slot
UE slot
BS slot
At BS
BS slot
BS slot
Prop. delay
Prop. delay
BS frame
BS frame
UE frame
Prop. delay
late
Timing advance information
Guard band
Prop. delay
Timing advance
BS frame
BS frame
UE frame
UE frame
UE frame
UE frame

## Slide 14: Active delay measurement
Another method, aimed at synchronising one basestation to another, uses active delay measurement using two-way signals:
eNodeB
Time Sync
(e.g. PTP, GNSS)
eNodeB
Estimate propagation delay from round trip time
Request to start synchronisation procedure
Accept
Signalling T2, T3
Over the air message at SFN1 start
T1
T2
Over the air message at SFN2 start
T4
T3

## Slide 15: Location-based methods
Passive compensation requires configuration of receiving device location (latitude, longitude, elevation)
  Good for stationary objects
  For moving objects, needs constant update
  Back to sensor fusion of PVT data – position, velocity, time

## Slide 16
Measurement Over The Air

## Slide 17: Measuring synchronisation over the air
If radio signals are being used for synchronisation, you’ll want to measure them, right?
Need to compensate for distance from eNodeB when calculating time error
  Use passive, distance-based compensation
  Non-invasive, doesn’t require physical access to equipment
eNodeB
Time Sync
(e.g. PTP, GNSS)
Primary, Secondary Synchronisation signals
radio frame
GNSS
Test set

## Slide 18
Conclusions

## Slide 19: Conclusions
Time is the fundamental, unifying dimension for sensor data
Synchronisation over the air interface extends accurate time to the customer
  The cellular signal itself becomes one of the sources of time
  Delay compensation required for accurate time
  PVT – position, velocity, time are inseparable
Measurement over the air verifies the entire synchronisation chain
Image: Royal Museums, Greenwich
The Greenwich Time Ball – the first “over the air” time signal (1833)

## Slide 20
Tim Frost,
Strategic Technology Manager,
tim.frost@calnexsol.com