## Slide 1
Pedro Antao | November 7th 2018
ITSF 2018
'PTP Profile Interworking'

## Slide 2
ITSF 2018
WRAP-UP ITSF 2017: 'The reality for Time and Phase synchronization within the Mobile Network Operator to address the LTE-A'
Evolve the transport network to support phase
PTP profile Interworking

## Slide 3
WRAP-UP ITSF 2017: 'The reality for Time and Phase synchronization within the Mobile Network Operator to address the LTE-A'
Solutions to enable phase & time being considered in the RAN
PTP G.8275.1 T-TSC + SyncE
PTP G.8275.2 T-TSC-P, with/without SyncE
GNSS + SyncE , contingency.
GNSS
PTP G.8275.1
GNSS
PTP G.8275.1
PTP G.8275.2
GNSS
PTP G.8275.1
PTP G.8275.2
2015
2016
2017
eNB (LTE-A)
In 2017, PTP ITU-T profile G.8275.2 seems to be a seriously solution for phase synchronization. Although G.8273.4 APTS and PTS has not been standardized.

## Slide 4
WRAP-UP ITSF 2017: 'The reality for Time and Phase synchronization within the Mobile Network Operator to address the LTE-A'
PTP G.8275.1 ETH L2 MCAST + SyncE (RAN T-TSC)
Standards finish in 2014
Feasible to leverage on centralized T-GM
Widely accepted by RAN vendors
Well defined metrics by the ITU-T
Requires full path support, not easy to achieve due to install based HW/SW restrictions
Legacy HW does not support
Slow start to IP routers vendors to support this profile
Notes: NOS use case , profile G.8275.1 is not easy to implemented due to MBH installed base HW… some hardware does not support PTP G.8275.1 profile, even support it is not compliant with G.8273.2

## Slide 5
WRAP-UP ITSF 2017: 'The reality for Time and Phase synchronization within the Mobile Network Operator to address the LTE-A'
Despite being standardized two years later than G.8275.1, it is already implemented and supported by a wider variety of equipment vendors
Does not requires full time path support
Asymmetry are more likely due to IP routing issues among parallel paths
Metrics are not well defined yet
More risky to leverage within centralized T-GM deployment
PTP G.8275.2 IP L3 UNICAST + “SyncE” (RAN T-TSC-P)
Distributed T-BC-P G.8275.2 (RAN T-TSC-P)
Notes: Combination of G8275.2 + SyncE depend from radio vendor.
Besides slide does not mention, test performed let us understand that RAN equipment with GNSS built-in does not implement G.8275.2 T-TSC-A

## Slide 6
WRAP-UP ITSF 2017: 'The reality for Time and Phase synchronization within the Mobile Network Operator to address the LTE-A'
PTP G.8275.2 APTS (RAN T-TSC-P)
Distributed Small/Mid size T-BC-A in the EDGE and/or Pre-AGG layers to provide higher scalability
APTS use the distributed GNSS reference, and centralized T-GM for backup with real time asymmetry correction
APTS

## Slide 7
WRAP-UP ITSF 2017: 'The reality for Time and Phase synchronization within the Mobile Network Operator to address the LTE-A'
GNSS receiver in the RAN
Risk of jamming
Installation and maintenance costs
Does not require synchronization features from IP/Transport Network
Easier to achieve +/- 1.5 us TE
Notes: Besides RAN Support SyncE and have builtin GNSS receiver, it is not clear that enhanced holdover is achieved under circumstances that GNSS fail with SyncE.

## Slide 8
WRAP-UP ITSF 2017: 'The reality for Time and Phase synchronization within the Mobile Network Operator to address the LTE-A'
PTP G.8275.1 trials, we have found a TE > +/- 1.5us due to DWDM asymmetries
DWDW path T-GM#1<>COI2 TE=+2.9us
DWDW path T-GM#1<>COI1 TE=-4.1us
RAN site A and RAN Sites B,C,D have a 7us TE

## Slide 9
WRAP-UP ITSF 2017: 'The reality for Time and Phase synchronization within the Mobile Network Operator to address the LTE-A'
STATEMENTS issued in 2017 to overcome the asymmetries found within the Network
  Re-engineer the DWDM non-coherent to coherent network, or embrace the DWDM within the sync chain.
  new optical segments are design to be coherent
  DWDM Sync functionalities are being evaluated, but without any decisions yet.
  Use asymmetry correction in the IP transport network
  Asymmetry correction features have been successfully validated, however it requires field measurement in every hop, does not scale!
    Deploy G.8275.2 T-BC-A
    No actions have been done
Please notice that phase synchronization has not been yet required, this might be valid till the 5G rollout.

## Slide 10
Evolve the transport network to support phase
NOS Synchronization network ASIS today (4Q18):
Geographically redundant centralized GrandMasters using GNSS reference;
Fully integrated with IP/MPLS transport network to glue the GrandMasters and Mobile Backhaul infra-structure to provide Frequency Sync over the Ethernet Physical Layer, either PTP packet sync;
Synchronization requirements is confined to Frequency due to FDD radio system (+/- 50ppb);
RAN is synchronized using SyncE, or PTP G.8265.1.
Most of the network devices are synchronized using SyncE.

## Slide 11
Evolve the transport network to support phase
NOS Synchronization network ASIS today (4Q18):
Despite the fact that:
GMs are G.8272 class A +/-100ns compliant, with RbXO oscillator for enhanced holdover;
T-BCs implemented within the IP Core and last generation Provide Edge Routers line cards are compliant with G.8273.2 Class A ;
However the:
Large amount of the line cards that provides MBH ETH-1G connectivity does not support PTP profile G.8275.1, neither compliant with G.8273.2;
Last mile access CSGs and MWs are not PTP aware.
Please notice, that routers compliant with T-BC class B’s have become available and introduced in the transport network in 2018. More recently witnessed that T-BC class C are being planned to become available mid 2019.

## Slide 12
Evolve the transport network to support phase
Solutions to support phase for the 4G
Due to 5G in the corner, the options to deploy timing phase shall be reviewed due new requirements regarding backhaul and fronthaul architectures!
5G is not only a new radio node, it a completely new network architecture!
…

## Slide 13
Evolve the transport network to support phase
Evolve from 4G eNB to 5G gNB Synchronization highlights
While the 4G eNB Synchronization fits on installed based backhaul using FTS leveraging on Profile G.8275.1, either PTS using Profile G.8275.2… for 5G we face new scenarios as explained next.
BBU architectures leverage on the following assumptions :
Local oscillator, typically a TCXO that synchronize to the Timing Synchronization references;
Timing Synchronization references are provided through the backhaul ETH-1G (S1 interface), or in alternative using an integrated GNSS receiver;
Distribute Sync to the radios: RRHs through the CPRI interfaces (timing is inherent to the CPRI interfaces;
Sync Requirements are frequency +/-50ppb and phase alignment +/-1.5us (phase requirement only required if CoMP or EiCIC is used) from a common reference UTC.

## Slide 14
Evolve the transport network to support phase
Evolve from 4G eNB to 5G gNB Synchronization highlights
The evolution to 5G, considers that BBU is Split into different entities: CU, DU, and some functions integrated within the RRU:
5G is TDD radio, and at the current being there is a consensus that RRUs sharing the same DU require +/-130ns Time Alignment, otherwise +/-1.5us;
Within the conceptual splits, the CU/DU S1 or DU F1, and RU shall interface the synchronization references, and both have their own high quality oscillators;
RRUs are expected to connect the DU over Ethernet using eCPRI or ROE, this interfaces shall be used to provide Packet Timing Sync as well!
While in the CPRI timing is inherent, in the packetized fronthaul (eCPRI, ROE) timing need to be explicitly transported to the RRU (eRE using CPRI terminology) therefore it requires PTP.

## Slide 15
Evolve the transport network to support phase
Evolve from 4G eNB to 5G gNB Synchronization highlights
Several 5G Synchronization architecture shall be evaluated:
gNB Synchronize from the backhaul or GNSS, and has integrated Boundary Clock features to provide sync to RRU’s.
Fronthaul Network provided timing sync to DU and RRU’s.
In resume, in the long term FTS using G.8275.1 seems to be the solution… meanwhile PTS is an alternative solution until network transport evolve to support full timing sync functions.

## Slide 16
Evolve the transport network to support phase
5G network architectures impose additional complexity that shall be used to define the synchronization strategy:
DRAN versus CRAN: BBU/RRU split CU/DU/RU and relationship with Synchronization;
5G RAN is TDD, Phase Timing synchronization requirements with tighter requirements than 4G LTE-A;
Fronthaul transport network (IEEE 1914.1 NGFI architectures);
Cloud Telco DC environment and Network Virtualization;
5G evolution paths: NSA vs SA and dependency from install base BBU’s;
Small Cell / Remote RU densification;
Synchronization standards being currently updated for 5G requirements.
Notes: NGFI architectures : node processing time
ITU-T G.8273.2 Class T-BC and T-TSC class C

## Slide 17
PTP profile Interworking
2a
2b
PTP Profile interworking have been included within ITU-T G.8271.2
Notes: Besides slide does not mention, test performed let us understand that RAN equipment with GNSS built-in does not implement G.8275.2 T-TSC-A

## Slide 18
PTP profile Interworking
PTP Profile interworking leverage on installed based FTS, and overcome HW limitations on the access network due to PTP not-aware of no compliance with G.8273.2
This architecture leverage on install based centralized T-GM’s and extend the PTP Full Time Support till the Edge, and extends the lifetime of existing Mobile backhaul solution until 5G network transformation starts.
FTS G.8275.1
PTS G.8275.2

## Slide 19
PTP profile Interworking
Status of the PTP profile interworking
Feature are becoming available for the IP router devices;
Performance measurement have been started, achieving good result.
Provides enhanced flexibility to provide phase synchronization across heterogenous network

## Slide 20
PTP profile Interworking
Other PTP interworking use cases might be interesting in the mobile as illustrated
gNB Synchronize from the backhaul or GNSS, and has integrated Boundary Clock features, optionally implement APTS.
With the IWF PTP Profile interworking, behave as T-BC with G.8275.1 towards the RRUs.

## Slide 21
‘PTP Profile Interworking’
Thank You!
pedro.antao@nos.pt