## Slide 1: Practical Implementation of a IEEE 1588 Based Synchronization Distribution System
Daniel Gallant – ITSF November 2018
Notes: 1

## Slide 2: Agenda
  Practical Implementation of a T-BC
  ToD Synchronization Between Master and Slave
  ToD Synchronization within the Network Element
  Challenges of Meeting 5ns Time Error
  Possible Solutions for Meeting 5ns and Beyond

## Slide 3: Implementation of a Telecom Boundary Clock (T-BC)
  Main physical components of a T-BC:
  Master and Slave PHY (ToD/timestampers)
  Processor (1588 stack & servo)
  1588 PLL (with DCO)
  SyncE PLL (independent from 1588 PLL)
  TCXO/OCXO (for frequency stability)
  Main functions of a T-BC:
  Packet processing (PTP stack, timestamping)
  PEC (uses timestamps to generate clocks)
  Physical layer clock (unaltered by PTP)

## Slide 4: The Goal of Network Synchronization
  All ToD counters within the timing chain must be synchronized with the T-GM:
  They contain the same time value
  They turn over at the same time (with nano-second accuracy)

## Slide 5: T-GM to T-BC ToD Synchronization
  Three stages of ToD synchronization:
  Initial adjustment: T-BC extracts ToD from 1588 packet sent by T-GM
  Lock acquisition: T-BC servo uses timestamp information to adjust ToD counter frequency minimizing time error
  Locked: T-BC servo makes fine adjustments of ToD frequency to keep time error at zero

## Slide 6: Option 1: T-BC ToD Synchronization –> Using a Physical Interface
  If timestamping is performed in separate physical locations within the T-BC…
  Synchronization of ToD at slave and master ports must be synchronized (or it will contribute to time error)
  Proprietary interfaces help ToD synchronization between PHYs

## Slide 7: Option 2: T-BC ToD Synchronization –> Using a Central ToD/Timestamper
  ToD and Timestamping can be located at a central point in the system
  Synchronization of ToD at slave and master ports must be synchronized (or it will contribute to time error)
  Or timestampers must reference a central point of ToD…

## Slide 8: Multi Circuit-Pack System Architecture
  Most carrier grade equipment is broken down into multiple circuit packs connected together with a backplane
  Timestamping/ToD and PTP stack functions (Line Card) are separated from the central clock generation functions (Timing Card)
  There’s still a need to synchronize ToD from the slave line card to ToD of master line cards

## Slide 9: Distribution of ToD across a Multi Circuit-Pack System
  ToD Distribution
  ToD from Slave line card is distributed to all Master line cards
  ToD is distributed over control plane
  Precision not important (1 second to get there)
  1PPS provides ToD 1-second rollover precision
  1PPS Distribution
  1PPS is generated by PLL/DCO (controlled by 1588 Servo)
  Objective is to align all 1PPS signals across all line cards
  Any 1PPS phase misalignment looks like constant time error (cTE)
  Challenges
  Backplane trace lengths must be matched or compensated
  Delay uncertainty of backplane drivers/receivers must be considered in timing budget
  I/O delay of line card PLL must also be considered

## Slide 10: Solution 1: Manual Calibration of 1PPS Distribution Path
  Backplane Trace Delays
  1PPS backplane trace delays are manually measured
  Variance in PCB trace length during manufacturing causes delay uncertainty
  Backplane Driver/Receiver Delays
  Driver + Receiver delay uncertainty over PVT : 2-3 ns typ
  Line Card PLL
  Keep I-O delay as low as possible by using ZDM
  All deterministic delays can be compensated for using adjustable delay at Line Card PLL.
  Challenges:
  Delay uncertainty from PCB traces, drivers/receivers, and Line Card PLL adds to the time error budget
  Drivers/receiver delay uncertainty is the main contributor
  PVT - Process/Voltage/Temperature,
  ZDM – Zero Delay Mode

## Slide 11: Solution 2: On-chip 1PPS Delay Measurement & Adjust
  Measuring 1PPS path delays
  1PPS path delays are measured at start-up
  Must be done for each Line Card (each 1PPS path)
  Delay measurement performed at central point in the system. In this case at the Timing Card.
  Could use existing SyncE backplane traces to provide return path
  Measured trace delay differences are adjusted at line cards
  1PPS delay = Round Trip Delay minus Return Path delay
  Advantage:
  Compensates for both backplane trace delay and driver/receiver delay uncertainty
  Challenges:
  Assumption that forward and return paths are symmetrical
  Return path must also be measured (using TxSyncE/RxSyncE pair?)

## Slide 12: Solution 3 - ToD Distribution Without 1PPS Distribution
  Synchronizes ToDB with ToDA without a physical time alignment signal (i.e. no 1PPS required)
  “1588-like” ToD distribution but with the advantage that Master and Slave are working from the same frequency (using existing backplane frequency distribution)
  No servo loop or acquisition process required
  1588 messaging “calculates” One Way Delay (OWD) and Time Error Offset (e)
  No PDV
  Static asymmetry (can be calibrated out)
  Challenges:
  Control plane must be 1588 aware (e.g. Transparent clocking)
  ToD transfer accuracy depends on timestamp resolution

## Slide 13: Conclusions
  Time error of a T-BC consist of PTP servo error + misalignment of ToD
  Distribution of ToD in a multi circuit-pack system takes careful design
  Meeting 5ns time error is a difficult challenge.
  New design practices and synchronization distribution architectures will be needed

## Slide 14: Thank You
Notes: 14