## Slide 1: Gateway Clock
November 2018
Samer Darras
Barry Dropping

## Slide 2: Agenda
IEEE 1588 Clock Types
Gateway Clock Overview
Time and Frequency Control Planes
Use Cases

## Slide 3: IEEE 1588 PTP Clock Types
Today there are 4 different IEEE 1588 clock types.
  Master Clock
  Boundary Clock
  Transparent Clock
  Slave Clock
There are many different IEEE 1588 PTP profiles in use today including industry specific profiles for:
  Telecommunications
  Power Utilities
  Enterprise
The current standard restricts PTP clocks to support a single protocol.
  A Boundary Clock must for example support the same protocol (PTP Profile) on its input side and its output side

## Slide 4: Gateway Clock – A New Clock Type
Industry requirements are expanding to require flexibility to support multiple evolving protocols for applications deployed today and for ones that will be required for the future
Modern clock systems are engineered to include multiple clock domains, and support multiple timing protocols
This gives rise to a new type of clock that can be described as a “Gateway Clock”

## Slide 5: Gateway Clock Functional View
Timescale
Generation
Network Isolation
Timescale Distribution
GNSS Services (GPS, Galileo, GLONASS, Beidou)
Protocol Services
(NTP, PTP, etc.)
PHY Signals (SyncE, T1/E1, TOD, 1PPS, 10MHz, IRIG, etc.)
Output Time and Frequency Services
Protocol Services
(NTP, PTP, etc.)
PHY Signals (SyncE, T1/E1, TOD, 1PPS, 10MHz, IRIG, etc.)
Time Transfer
Test Point (1 PPS)

## Slide 6: Gateway Clock – Multiple Control Planes
A Gateway Clock generates traceable time and frequency outputs:
Source for Time Control can be different than Frequency Control
The frequency control plane stabilizes the local oscillator to support enhanced time control
Frequency and Time control operate simultaneously
Traceability Control can mitigate path asymmetry on a PTP input reference
Traceability Control Plane
Phase/Time Control Plane
Frequency Control Plane

## Slide 7: Gateway Clock Use Cases

## Slide 8: Communications Use Case for a Gateway Clock
MTSO/CRAN
Backhaul
CPRI
Fronthaul
RE
REC
Data Center
Midhaul
PTP Grandmaster
Clock (PRTC)
Small Cells
Synchronization Management
Core
Aggregation
Edge
Backhaul
NB
Timescale
Generation
Network Isolation
Timescale Distribution
Time Transfer
Gateway Clock
PTP G.8275.2
PTP G.8275.1
In this example the Gateway clock is providing protocol translation from G.8275.2 to G.8275.1

## Slide 9: Data Center Use Case for a Gateway Clock
Many Data Centers are in Colocation environments where it is not possible to install GNSS
Advanced data centers require highly accurate stratum 1 level NTP
  Stratum 2 NTP is generally not accurate enough for the today’s data center needs
In this case a Gateway Clock can be installed inside the Data Center
  Highly accurate PTP can be received from a remote PTP master, and translated to NTP to serve the data center
NTP
Timescale
Generation
Network Isolation
Timescale Distribution
Time Transfer
Gateway Clock
PTP Grandmaster
Clock (PRTC)
PTP

## Slide 10: Conclusion
A well designed “Gateway Clock” can provide timing protocol translation for flexible deployment
Gateway Clocks can select from multiple input reference types to establish independent Time and Frequency control planes
Many use cases can benefit from Gateway Clock functionality

## Slide 11: Thank You