## Slide 1: Deploying Phase Synchronisation. When strategy met reality.
3rd November 2020

## Slide 2: Contents
About EE – A typical operator (?)
Backhaul strategy for deploying 5G
  Requirements
  Architecture
The end?
More requirements
Some tactical options
The end.

## Slide 3: About EE
Commercial
EE was a UK limited company formed by the merging of Orange UK and T-Mobile UK, operating 2G, 3G and 4G networks providing consumer and business services, and developing the Emergency Services Network (ESN).
EE was acquired by BT in 2016, and became fully assimilated as a brand of BT Consumer, alongside the BT and Plusnet brands.
BT launched the UK’s first 5G service under the EE brand in May 2019, covering 16 cities at launch and 80 cities and towns within a year.
Technical
T-Mobile UK had built a 3G RAN on a platform shared with 3UK. Orange UK 3G was integrated onto the same platform following the merger that created EE.
Later, both 3UK and EE built their own 4G RANs sharing the same sites and backhaul.
BT, having integrated the EE and BT design communities, developed and deployed a new strategic end to end 5G solution (though still sharing sites), including a new phase synchronisation platform.
A BT brand and the UK’s biggest mobile operator

## Slide 4: Strategy for deploying 5G
EE had previously deployed 4G as an additional RAN layer over its 2G and 3G networks using the existing backhaul architecture and infrastructure, albeit with capacity upgrades.
Why couldn’t this approach be adopted for 5G?
The step change in capacity required is beyond some of the technologies in the existing backhaul, especially microwave radio in the traditional bands.
Delivering low-latency with distributed service platforms requires a different architecture, with IPSec gateways distributed away from the centralised core of 4G.
Last but not least, 5G would be the first deployment of TDD spectrum for EE and would require accurate phase synchronisation. Although previous evolutionary steps were effective in delivering 3G and 4G, there was a legacy of a wide variety of different transmission products which would require a massive design and test effort to add phase synchronisation support. Some were simply not capable.
Revolution is required.
Evolution or revolution?

## Slide 5: Requirements for 5G
Transport
  >1Gb/s capacity to each base station (10Gb/s interfaces)
  Low latency transmission
  Low latency architecture with any-any connectivity close to the network edge for early turn-around and access to distributed service platforms.
Phase synchronisation
  ±1.5µs to be achieved at air interface.
  On-path support throughout (G.8275.1)
  Common source synchronous Ethernet for holdover support
  UTC aligned for inter-operator interference avoidance
What should the backhaul revolution deliver?

## Slide 6: Strategic backhaul architecture
10G over WDM/fibre to cell site, possibility of subtending child site using high capacity mm wave radio transmission
MSE providing VPN access into core, or local turn-around and access to distributed service platforms
PRTC/GM co-located or one hop (direct fibre) to MSE. Local GNSS (UTC aligned) with backup via networked synchronisation.
Synchronous Ethernet frequency and G.8275.1 profile phase from PRTC to base station.
mmW
5G
CSG
WDM
10G/λ
WDM
10G/λ
MSE
Cell site (1000s)
Tier 1 (100s)
PRTC
PRTC
mmW
5G
Telecom Boundary Clock, T-BC
NTE
Metro (10s)
NTE
Synchronisation Platform
Telecom Time Slave Clock, T-TSC
Telecom Grand Master T-GM
Physical layer connectivity

## Slide 7: The End?

## Slide 8: Deploying phase synchronisation
Wherever 5G is deployed, the new strategic backhaul architecture will also be deployed because capacity and service requirements dictate, so phase synchronisation will be delivered wherever it is needed? Time for a reality check…
ENDC
  Creates a need for (looser) phase synchronisation for 4G base stations in 5G coverage.
5G on legacy backhaul
  Decoupling 5G RAN deployment from strategic backhaul deployment to maintain contiguous coverage.
Job done? Not quite.

## Slide 9: ENDC
Where operators have an existing 4G network, 5G is usually deployed with dual connectivity allowing the benefits of New Radio to be realised before implementing an entire 5G core.
A user device with separate 4G and 5G radio chains would be able to communicate simultaneously via 4G and 5G base stations. However optimisation of device cost, power consumption and size has resulted in sharing of components such as RF power amplifier and typical devices require non-simultaneous access to 4G and 5G. This imposes a need for phase synchronisation on 4G, even if FDD, although looser at around ±0.5ms.
Co-located 4G base stations have phase synchronisation available from the strategic backhaul solution.
4G base stations not co-located with a 5G base station but on the edge of 5G coverage will need to participate in ENDC, but will not have access to phase synchronisation from the strategic backhaul solution. Another solution is needed, but only for the looser ±0.5ms requirement.
EUTRAN/New Radio Dual Connectivity

## Slide 10: 5G on legacy backhaul
5G rollout will be driven by service capacity demand and also by marketing goals, which may be different.
Base station deployment may go ahead of transmission (new fibre routes can take a long time).
There is a risk of ending up with patches of 5G coverage with gaps, either permanently if not demand driven or temporarily if resulting from transmission delivery delays.
These coverage gaps could be filled in by enabling 5G on legacy backhaul. Again, these will not have access to phase synchronisation from the strategic backhaul solution. Another solution is needed, but this time the full ±1.5µs accuracy is required.
.
EUTRAN/New Radio Dual Connectivity

## Slide 11: Tactical phase synchronisation
As set out at the start, in a backhaul network that has evolved over time alongside introduction of new RAN technologies, there will be many types of equipment and it may be impractical (or impossible) to add on-path phase synchronisation support. Fortunately, there are some relaxations in the requirements:
Lower availability than the strategic solution is acceptable
For 4G FDD, much looser accuracy is acceptable (±0.5ms)
This makes some options available that wouldn’t be used in the strategic case:
4G FDD ENDC
  Base stations own GNSS solution on single sites.
  Mini –PRTC GNSS solution in clusters linked by any practical number of microwave radios without on-path support.
5G
  Base stations own GNSS solution on single sites
  Mini –PRTC GNSS solution in clusters where there is no more than one microwave link without on-path support to each 5G base station.
Options for legacy backhaul.

## Slide 12: Conclusion
For a typical operator, new backhaul will be required for 5G
New backhaul can easily incorporate a high accuracy, high availability phase synchronisation solution
Phase synchronisation will probably be needed in places where the new backhaul isn’t (yet) deployed
There will be tactical options for phase synchronisation without new backhaul

## Slide 13: The End.