## Slide 1
How to Design a PTP Grandmaster for Automotive Applications
Nikolaus Kerö, Heiko Gerstung

## Slide 2: Modern Vehicle Communication Systems (I)
More than 80 ECUs controlling a multitude of functions / features
Several Sub-Systems / Tasks
  Engine Management
  Safety
  Comfort
  Entertainment
New Requirements
  IVE – In-Vehicle Experience
  ADAS – Advanced Driver Assist Systems
    Cameras, Radar, LIDAR, ultrasound, …
  ICNS – In Cabin Monitoring Systems
  Automatic Driving
  Fully autonomous driving

## Slide 3: Modern Vehicle Communication Systems (II)
Requirements for Communication Media
  Cheap & Light-weight (literally)
  Reliable and fault tolerant (at times)
  Hard real time
  Extremely stringent EMF Resilience
  Low power consumption
  Limited cable length (<40m)
=> Numerous legacy bus systems have evolved
  LIN, CAN, Flexray, …
Physical media is optimized to the specific task
  1-wire, twisted pair, fibre, …
Protocols likewise so
  Inherent synchronous
  Guaranteed bandwidth and latency

## Slide 4: Modern Vehicle Communication Systems (III)
Legacy busses have fixed bandwidth limitations
ADAS requires multiple sensor inputs at high rates
  Fully autonomous driving even more so
Let’s switch to Ethernet as everybody else did
Ethernet for Automotive
  100/1000Base –T1
    Single twisted pair
    Max 40m
  TSN … Time Sensitive Network
    PTP (IEEE802.1AS)
    Scheduling and traffic shaping IEEE802.1Qxxxx

## Slide 5: Automotive requirement
A car is a hostile environment for every electronic circuit
  Temperature range -40°C … 120° (150°C)
  Subjected to vibrations
  Power supply
    7V … 15V (24V)
    Surges up to 35V (even 70V)
  Stringent limitations
    Power consumption
    Size
  “instant-on” i.e. no long boot times!
  Extremely harsh EMC constraints
    Emissions & Immunity 10 kHz … 18 GHz
  ESD
  ….

## Slide 6: Block Diagram of a Modern PTP GM Re-visited
Power Supply
90V-240V
Power Supply
90V-240V
Back Plane
Multi Band
GNSS Receiver
Control CPU
USB
Ethernet
PTP
(NTP)
Module
1G Cu
1G Fibre
1PPS
PTP
(NTP)
Module
10G Fibre
IO
…
Clock
Module
CPU
Embedded Linux
FPGA
PHY
RAM
ROM
Clock, Control

## Slide 7: PTP GM for Automotive – an overkill?
TSN
  Provide sub-µs accuracy for all devices
  Allow reliable scheduling and thus support hard real time requirements
Do we really need an absolute notion of time?
Logging
Postmortem failure analysis
Any 802.1AS device can provide stable but arbitrary time information
Vehicle will exchange critical data
  Other vehicles
  Roadside equipment

## Slide 8: PTP GM for Automotive
Single Chip solution for PTP
  PTP Hardware modules
  Embedded CPU (bare metal)
  Support for TSN scheduling and traffic shaping
Oscillator ???
  Crystal Oscillators affected by vibrations
   MEMS based oscillators (SiTime)
100/1000Base-T1
GNSS signal via antenna splitter
Size … 70mm x 70mm, Power consumption … 4W
Only 3 - 4 integrated Components: FPGA, PHY, Flash, (GNSS timing receiver)
  All available in automotive temperature grade

## Slide 9: Conclusions
Automotive Ethernet comes with TSN and thus PTP
Absolute time will become mandatory
Existing designs cannot be simply adapted for automotive use
Fully integrated solutions are key
  Single chip PTP device
  Minimal number of external components
  Small form factor
  Meeting all major automotive specifications
If you are interested or have suggestions and ideas, please get in touch with us.

## Slide 10
Thank you for Your Attention
keroe@oregano.at