## Slide 1: Class D – Can We Achieve It?
A look at the Challenges of a T-BC
David Spencer – ITSF 2020

## Slide 2: Network and Equipment Limits
Operators care about the end-to-end performance
  Network Limit
A Telecom Boundary Clock (T-BC) vendor only controls their portion
  Equipment Limit
Standards are crafted so that building a defined network with devices that meet the equipment limit will ensure the network limit is met

## Slide 3: T-BC Classes
Not all networks are the same
  Different size
  Different application
To provide flexibility ITU-T G.8273.2 defines four classes of T-BC
  Different performance for different networks and applications
  Differences relate to performance only
T-BC Class | Intended Application | Network Size | End-to-end Performance
A | Backhaul | Short (10 hops) | 1.5 µs
B | Backhaul | Long (20 hops) | 1.5 µs
C | Fronthaul | Very short (5 hops) | 130 ns
D | Flexible | Very long | Application Specific

## Slide 4: T-BC Performance Limits
Parameter | Measurement | Class A | Class B | Class C | Class D
Max ¦TE¦ | Unfiltered | 100 ns | 70 ns | 30 ns | -
Max ¦TEL¦ | Low pass | - | - | - | 5 ns
cTE | Averaged | 50 ns | 20 ns | 10 ns | -
dTEL (MTIE) | Low pass | 40 ns | 40 ns | 10 ns | -
dTEL (TDEV) | Low pass | 4 ns | 4 ns | 2 ns | -
dTEH | High pass | 70 ns | 70 ns | - | -
 Class B is Class A with tighter cTE requirement
 Class C tightens both cTE and dTE over Class B
 Class D limits are so small that only a single overall number is specified (currently)

## Slide 5: Distinguishing cTE vs dTE
dTE:
  Averages to zero over a long enough period
  Can therefore be filtered (in theory)
  Typically uncorrelated between nodes so doesn’t accumulate
  Relates to precision: Time stamping resolution and local clock stability
cTE:
  Doesn’t change over meaningful time period
  So cannot be filtered
  Accumulates node to node
  Relates to accuracy: Time stamping static error (PHY & clock distribution errors)
cTE is our enemy – accumulates across nodes and cannot be filtered

## Slide 6: cTE: The challenge
To reduce cTE, timestamping must be accurate
  Capture exact time that frame comes off the wire
But a real system has inaccuracies
  Delay in PHY between frame arriving and timestamp trigger
  Distribution delay from local clock to timestamper
PHY delay is a function of PHY design
  Select a part with small delay variation
Distribution delay is a bigger problem …
  … and what we’ll look at here

## Slide 7: Hypothetical Model vs. Reality
Disconnect between model and reality
  Implementation has to deal with architecture distributed across multiple cards in a chassis
How ITU-T sees a T-BC
What a typical T-BC looks like

## Slide 8: 1PPS Distribution: Time Alignment and Delay Handling
CONFIDENTIAL SILICON LABS
    ΔT delays are adjusted to achieve  (ΔTs + δS) = (ΔTm1 + δ1) = (ΔTm2 + δ2) = ΔTt
    Servo adjusts Ttc to achieve  Tlcs (local time) = Tm (master’s time)
      Ttc == Tm + (ΔTs + δS)
      ie Timing card ToD will lead actual time by 1PPS backplane delay to the slave line card + the configured 1PPS input delay on the slave line card
      Since ΔTt = (ΔTm1 + δ1) = (ΔTm2 + δ2) = (ΔTs + δS) therefore Tt, Tlcm1 and Tlcm3 will all be aligned with Tm

## Slide 9: Solution 1: Manual Calibration of 1PPS Distribution Path
  Backplane Trace Delays
    1PPS backplane trace delays are manually measured
    Variance in PCB trace length during manufacturing causes delay uncertainty
  Backplane Driver/Receiver Delays
    Driver + Receiver delay
  Line Card PLL
    Keep I-O delay as low as possible with zero-delay mode
    All deterministic delays can be compensated for using adjustable delay at Line Card PLL.
  Challenges:
    Delay uncertainty from PCB traces, drivers/receivers, and Line Card PLL adds to the time error budget
    Drivers/receiver delay uncertainty is the main contributor

## Slide 10: Solution 2: On-chip 1PPS Delay Measurement & Adjust
  Measuring 1PPS path delays
    1PPS path delays are measured for each card at start-up
    Delay measurement performed at central point in the system. In this case at the Timing Card.
    Could use existing SyncE backplane traces to provide return path
    Measured trace delay differences are adjusted at line cards
    1PPS delay = Round Trip Delay minus Return Path delay
  Advantage:
    Compensates for both backplane trace delay and driver/receiver delay uncertainty
  Challenges:
    Assumption that forward and return paths are symmetrical
    Return path must also be measured (using TxSyncE/RxSyncE pair?)

## Slide 11: Conclusion
Class D is tough
  5 ns total time error to cover:
    PHY delay variability in slave port
    Alignment of slave port timestamper to local clock
    Alignment of each master port timestamper to local clock
    PHY delay variability in each master port
    … and any low frequency dynamic errors
But we can do it if we have:
  PHYs with very well controlled internal delays
  Carefully designed clock distribution networks supported by timing ICs that feature
    Programmable per-input delays
    Internal delay measurement and compensation
    Two-way (feedback) delay measurement
    Multiple outputs to eliminate external fanout buffers