## Slide 1: Clocking the Cloud Timing in Datacenters
Bryan Hovey
ITSF 2021

## Slide 2: Agenda
Why do Datacenters need precision time?
Example deployment
Making sure it works
2
calnexsol.com

## Slide 3: Why do Datacenters need precise time?
Don’t ask me, ask this guy –
https://www.youtube.com/watch?v=JK3eTGkX6qY

## Slide 4: Why do Datacenters need precise time?
What ‘this guy’ said (cont’d):
1,000,000 computers
If all the computers are sync’d, they can compute and make decisions faster
The greater the precision of sync, the faster the decisions can be made
∴ SPEED & CAPACITY
1 computer computes
1 computer computes
2 computers

## Slide 5: Why do Datacenters need precise time?
What ‘this guy’ said (cont’d):
1,000,000 computers compute
‘Man-made’ 20ms delay ensures no computer thinks it’s getting data from the future
Precisely sync’d computers mean this 20ms delay can be dropped
20ms delay

## Slide 6: Why do Datacenters need precise time?
More cool ideas:
  Telemetry on a global scale – performance, latency, etc.
  Event logging for troubleshooting or optimisation
  AI – decision making needs data order integrity (which is first?)
  Reduced data exchange (I trust the other computer)
  Enable lower spec components?
  Q: Who’s driving? A: Cloud
  Etc.

## Slide 7: Example deployment
Open Compute Project (OCP) Time Card project is an example of delivering microsecond accuracy to any x86 machine with a HW-timestamp enabled NIC via PTP
Other projects also looking at SyncE and White Rabbit in addition to PTP
Datacenter PTP Profile developed within OCP
Source: Facebook Engineering
GNSS
Meta
Time Card

## Slide 8: Datacenter PTP Profile No.1 - OCP
Figure 1.
Model 1 – Chain of
Transparent Clocks
Network Fabric Layer
Time Reference Layer
GNSS
GM
TC
TC
TC
TC
Server Layer
OC
Source: OCP

## Slide 9
Why testing/monitoring is required now
Moving from 100ms accuracy to 1µs accuracy – timing and synchronisation becoming more critical for Datacenters
Moving from NTPd to more precise NTP and PTP
For example, from Datacenter PTP Profile No. 1 Model 1 (OCP):
  The maximum time error between any two OCs must be within ± 5 µs
  The maximum time error between a GM and any OCs must be within ± 2.5 µs
  The maximum time error generated by a TC must be within ± 100 ns
  Etc.
100ms accuracy didn’t need to be verified. Testing is essential to validate µs accuracy

## Slide 10: Example deployment
GNSS
Independent timing monitor for 1PPS, PTP, NTP, SyncE
Automated operation, centralised management
Provides data for pre-emptive or forensic purposes
Timing Monitor
Source: Facebook Engineering
Meta
Time Card

## Slide 11
Bryan Hovey
bryan.hovey@calnexsol.com