## Slide 1: Future Time and Frequency Technologies for Defence
Matthew Aldous
DSTL Quantum Sensing Team
ITSF
2nd November 2021
DSTL/CP134404
Crown copyright (2021), Dstl

## Slide 2: The Dstl Quantum Sensing Project
To be world leading in the engineering of Quantum Sensing Systems; understand the impact for Defence and Security, and pull through technologies from the National Quantum Technology programme.
Attribution: (left to right) cold atom accelerometer: Imperial College / M Squared Lasers, MEMS gravimeter: University of Glasgow / Optocap, MINiature Atomic Clock (MINAC): Teledyne-e2v / National Physical Laboratory, cold atom gravity gradiometer: Teledyne-e2v / University of Birmingham

## Slide 3: Some Dstl-led challenges in Sensing and Timing
Alt-PNT demos 2024 and beyond
Bi-static radar demos
Deployable GPS-performance clock
Optical time transfer
Atomic vapours
Cold atoms
GNSS resilience

## Slide 4: Military Time
Military time analysis – 2015
“GPS is already a ubiquitous location and time source deployed on the battlefield and shall be used as the platform master clock”
Blackett – 2018
“GNSS presents a potential single point of failure affecting multiple services and
applications”

## Slide 5: Robustness
All military equipment needs to survive, and often function in an environment with some combination of:
  Vibration
  Mechanical Shock
  High temperature
  Low temperature
  Fluids – Water, fuel, lubricants
  Radiation
  Electrical noise – conducted & radiated
  Magnetic noise
  Fungal ingress (yes- really)
OFFICIAL

## Slide 6: Extramural Research
UK OFFICIAL
We have colleagues who can help us build for this…

## Slide 7: Extramural Research
UK OFFICIAL
PhD students
  26 studentships at 8 institutions
  4 of which are directly applicable to future clocks or enabling technologies
Industrial partners
  6 projects at 5 organisations
  3 of which are directly applicable to future clocks or enabling technologies

## Slide 8: Intramural Research
UK OFFICIAL
…but sometimes there’s no substitute for doing it yourself…

## Slide 9: Motivations: overall
Explore and develop quantum S&T for defence and security applications
First hand experience to disentangle hype from real opportunities
Understand and solve engineering challenges
Support trials and stakeholder demonstrations
Ensure MOD is an intelligent customer
Actively contribute to the UKNQTP and sovereign capability

## Slide 10: Motivations: in detail
Deployable solutions: optical transitions in atomic vapour
Time-scale development: supporting development of National Timing Centre (NTC)
Preparing for an optically-defined second: transportable optical lattice clock
Intelligent customer: independent test and evaluation capability
100ns
1ns

## Slide 11: Time and Frequency Experiments
Miniature Optical Lattice Clock (OLC)
  Developed with Uni of Birmingham and NPL
  Rack-sized Strontium lattice clock
  Developing integration technologies and improving robustness
Strontium Flywheel Clock
  Vapour-based optical reference to support OLC during dead-time
  Developing strontium vapour cell fabrication technology
Iodine Vapour Optical Clock
  Robust optical frequency reference
  Exploring practical use of compact and low SWAP laser sources
  Future focus on integration and miniaturization
Dstl photo at UK OFFICIAL taken in QS lab.
Notes: Dstl photo at UK OFFICIAL taken in QS lab.

## Slide 12: Clock Development: Iodine
Starting point for in-house optical clock development, using Modulation Transfer Spectroscopy in a vapour cell
Aiming for performance superior to Cs beam tube in comparably-sized package
One key objective is to build expertise
Clock laser lock achieved, undergoing optimisation and miniaturisation
Dstl photo at UK OFFICIAL taken in QS lab.
Notes: Dstl photo at UK OFFICIAL taken in QS lab.

## Slide 13: Clock Development: Sr Vapour
Optical frequency standard using intercombination line (689nm) as frequency reference
Low TRL: Sr beam systems exist in the literature, but no vapours
Extremely challenging materials science: high temperature, highly corrosive strontium vapour
Potential synergy with Sr OLC as pre-stabilisation of red MOT laser (“flywheel clock”)
Dstl photo at UK OFFICIAL taken in QS lab.
Notes: Dstl photo at UK OFFICIAL taken in QS lab.

## Slide 14: Clock Development: Optical Lattice
Continuation of 5-year project with University of Birmingham and NPL to achieve:
  fractional stability of 1x10-15 at 100s
  packaging suitable for road transport
  low-maintenance operation
System delivery to Dstl enables further development and direct in-house exploitation
Continued support between partners
Dstl photo at UK OFFICIAL taken in QS lab.
Notes: Dstl photo at UK OFFICIAL taken in QS lab.

## Slide 15: Clock Development: Optical Lattice
Lattice clock developed in three modules at two sites
  All three subsystems demonstrated operating in at least two locations
  Transportability test of physics package – lattice trap recovered just 3 hours after a 65km drive
  Whole clock now located at Porton for further development and ruggedisation
Images courtesy of UoB, provided under full rights
Dstl photos at UK OFFICIAL taken in QS lab.
Notes: Left: Images courtesy of UoB, provided under full rights. Middle, right: Dstl photos at UK OFFICIAL taken in QS lab.

## Slide 16: Test and Evaluation
Test equipment
  GPS time server for PTP/NTP
  GPS disciplined oscillator
  Phase noise measurement kit
  Cs beam tube references
  Commercial cold Rb references
  Ultra-stable quartz oscillator
Plans for environmental control to extend test capabilities
Dstl photos at UK OFFICIAL taken in QS lab.
Notes: Dstl photos at UK OFFICIAL taken in QS lab.

## Slide 17: Test and Evaluation
COTS performance and resilience
  Specification assurance (now)
  Climatic variations (2021/2022)
  Vibration resilience (2021/2022)
  AC/DC magnetic fields (2021/2022)
Dstl photos at UK OFFICIAL taken in QS lab.
Notes: Dstl photos at UK OFFICIAL taken in QS lab.

## Slide 18: Technology Development Challenges – Common Issues
Maturing low Technical Readiness Level (TRL) technology is notoriously challenging:
combination of technical complexity of underpinning science;
lack of common, contextual understanding for opportunities and constraints.
Information exchange is hampered by inability to release information on Defence and Security Requirements to external industry and academic parties
Most requirements, Def Stans etc. are higher than OFFICIAL
Academia and Small & Medium sized Enterprise not cleared to receive or hold higher classifications
Establishing an evidence base for comparison and direction of targeted investments against identifiable requirements.
A common ‘language’ is needed to allow technical specialists, industry suppliers and military capability leads to convey opportunities and constraints.
Common Issues
Potential Solution

## Slide 19: ESL Matrix Mapping Technology Capability to Platform Requirements
Platform requirement profile is mapped onto technology capability, highlighting:
Areas where the technology meets platform requirements
Areas requiring further technology development
Roadblocks, where a technology could be fundamentally limited and unable to meet platform requirements
Limited capability in platform environment
Technology requires further development to meet platform requirements

## Slide 20: Quantum technology and DASA
Recently completed focused call on reducing reliance on GNSS
Assessed using Engineering Severity Level (ESL) tool
DASA Open call provides a route for funding

## Slide 21: Thank you
…come and talk to us at the conference, or
…contact us at QuantumSensing@dstl.gov.uk
If you still have questions…

## Slide 22
Content includes material subject to © Crown copyright (2021), Dstl. This material is licensed under the terms of the Open Government Licence except where otherwise stated. To view this licence, visit http://www.nationalarchives.gov.uk/doc/open-government-licence/version/3 or write to the Information Policy Team, The National Archives, Kew, London TW9 4DU, or email: psi@nationalarchives.gov.uk