## Slide 2
Maintaining Precision Time
in a Diverse Financial Trading Environment
Paul O’Halloran CEng MIET
Notes: Welcome
Brief bio
Non-technical dive into the challenges of precision time in banking

## Slide 3
Why is Precision Time Needed in Finance?

## Slide 4
Performance and Regulatory Requirements
High frequency, low latency trading
Bespoke high performance, low ‘tick-to-trade’ system response times. Precision time (<10µS) is used to provide latency performance monitoring of individual components within the system.
Typically a high touch operational environment with dedicated dev-ops team.
Transaction timestamping
Transaction timestamping precision obligations developed for trade forensics by regulators. Notably MiFID II in Europe and FINRA Consolidated Audit Trail (CAT) in the US.
Applies to all transaction systems within the jurisdiction and relevant to the general compute environment for financial organisations.

## Slide 5
Timestamp/system clock precision requirements
MiFID II: Annex I: RTS 25
Summary of RTS 25 transaction timestamp precision to UTC (max divergence):
  High frequency trading 100µS
  General compute transaction 1mS
  Human transaction 1S
FINRA Rule 6820 – Consolidated Audit Trail Clock Sync
Summary of CAT NMS Plan S6.8 Clock Synchronization timestamp tolerance to NIST:
  Venue general compute transaction 50mS

## Slide 6
Timestamp/system clock precision requirements
MiFID II: Annex I: RTS 25
Summary of RTS 25 transaction timestamp precision to UTC (max divergence):
  High frequency trading 100µS
  General compute transaction 1mS
  Human transaction 1S
FINRA Rule 6820 – Consolidated Audit Trail Clock Sync
Summary of CAT NMS Plan S6.8 Clock Synchronization timestamp tolerance to NIST:
  Venue general compute transaction 50mS
Notes: SEC Rule, 613 Audit trail requirements
CAT NMS: Consolidated Audit Trail National Market System Plan – industry implementation plan
Focusing on the general compute environment

## Slide 7
Assurance and reporting
The evidencing of timestamp precision assurance, compliance, and the reporting of non-compliance, is as important to the delivery of precision time within the service.
MiFID II RTS 25, Article 4, states that traders:
  shall be able to demonstrate traceability to UTC (≤ annually)
  identify the exact point at which a timestamp is applied
  demonstrate that the timestamps remain constant
FINRA CAT:
  self certification of compliance (annually)
  logging of clock synchronization, retention 5 years
  CAT Alert – 2020-02 amendment states threshold exceedance reporting:
  self reporting of significant violations from clock sync threshold
    by absolute deviation (≥ 2x threshold or 100mS)
    by persistent deviation (≥ 10 instances in rolling 24hr)
Assurance and evidencing
Notes: Periodic and ongoing evidencing clock-sync precision and reporting fundamental to compliance with regulations

## Slide 8
Clock-sync operations in diverse DC environments

## Slide 9
Engineering and deploying end-end solution
Application consumable system time budgeting
Delivering precision time from GNSS (i.e. GPS) or terrestrial (i.e. NPLtime) into a datacenter is only half the story. For an enterprise the greatest challenge is achieving and maintaining assured time which can be easily consumed by applications across diverse environments, infrastructure, server hardware generations and OS stacks.
The objective is to achieve system time within tolerance at every gettimeofday() or GetSystemTime() call. In terms of precision budget for 1mS:
Datacenter clock source 50µS 5%
Local transport (i.e. PTP) 50µS 5%
Disciplining local system clock 400µS 40%
Operating margin 500µS 50%
Notes: GPS generally accepted as valid UTC source UTC(USNO) top tier
NPL offering NPLTime testrial time services – Dr Leon Lobo. NIST understood to be developing similar service.
Half of operating safety margin, server stack gets 80% of remaining with clock and network sharing the remaining 20%
GetSystemTime() Windows
Clock signal may be considered as incurring additive phase noise through the system.
gettimeofday() Linux Unix
@ 10Gb an Ethernet packet serialization delay ~ 1µS
Transport on network significantly effected by WAN & firewalls

## Slide 10
Ongoing challenges
Solution license models
Where the clock-sync solution requires software components on the end-system there is friction between operational and commercial risks, and compliance obligations. This becomes heightened where the component is licensed under ‘untrusted’ model – i.e. the component ceases to function when license expires or not present (license failure).
Regulatory risk
License/Op risk
Commercial risk
Minimal license failure impact.
May be generally deployed to reduce variation and cost in the environment but at potential higher licensing cost.
“Trusted” license model
Regulatory risk
License/Op risk
Commercial risk
License failure leads directly to near-immediate system and application failure and becomes a dominant consideration in design and operation. Not for general deployment.
“Untrusted license model”
Notes: Trusted
Licensed instances may be over spec’ed or under spec’ed
over – commercial risk to the user
under – commercial risk to the vendor
Untrusted
License driven operational failure dominant consideration. Residual risk to key business/transaction applications.

## Slide 11
Ongoing challenges
VM mobility
Within DC virtual environments it is often common practice to move virtual machine (vm) between hosts to balance workloads during the production period using vm mobility methods (e.g. Vmware’s vMotion). This is generally achieved by transferring a snapshot of the vm’s running state.
vm mobility typically causes a c. 500mS freeze of the vm instance and hosted applications
  caused by vm snapshot, transfer and restart with the subsequent system clock lag
re-sync of the restart system clock to within desired tolerance is not instantaneous
  vm system can be synced to the host time on restart which can reduce the initial sync error
  the hosted applications which require transaction timestamp likely exceed the 50mS & 1mS regulatory thresholds for a period during full re-sync
Notes: Generally vm host platforms sync’ed to DC’s NTP time source – not precision time source,
Restarted VM will take on host’s NTP time
Root cause: hosting platform sync
May also be consideration in certain DR/BCP models dependent on vm mobility

## Slide 12
Ongoing challenges
Managing change - application and server lifecycle churn
Datacenter system hardware in the enterprise has a typical lifespan of c. 7 years. This often aligns to significant application changes to the stack or re-architecture. Taking this lifecycle on the macro scale, enterprise datacenter is typically being churned at a rate of c. 14% p.a..
Where precision solution is not generally deployed the challenge is to maintain the coverage through the ongoing change cycles. Infra designers, developers and application owners may not be fully aware of the underpinning precision time service requirements.
Combined top-down and bottom-up approach to manage the non-compliance risk.
  Use of CMBD as single point of truth to record the applications, instances and hosting end-systems identified as requiring precision timestamping
  Periodic validation of end-system compliance (as per CMDB assertion) through reconciliation with end-system performance logs
Notes: Right sizing of regulatory reporting scope key - especially regarding compliance reporting (FINRA CAT).
Do not want to under report – gap
or over-report on systems not in scope - regulatory liabilities on system issues
Feedback loop – deployed view through logs against asserted state from CMDB

## Slide 13
Desired Future State

## Slide 14
Assured time services
The development of assured precision time delivery services is desirable to eliminate the need for the sync assurance process wraps within organisations.
Strategic wish list
Reduction in component build variation and complexity
Reduce the variation in hardware, software and OS across the data centre estate through simplification.
Notes: Assured time services – conversations with Dr Leon Lobo, NPL about research and development in this space Defer to initiatives presented at conference
.
Drive to normalise precision time services to reduce overall cost and risks
Reduce variation -Dr Edwards Deming stated increased variation can lead to increased cost.

## Slide 15
The current solutions for delivering precision time services in the cloud are mostly overlay, where the customer builds and runs services on generic cloud components, rather than leveraging native service provider offerings.
Need cloud native precision clock sync services
remove pinch-point in the migration of transaction applications to cloud introduces
reduce build variation and complexity with subsequent cost and risk reduction.
Moving applications to public cloud
Move to precision clock sync capability to the underpinning virtualization platform hosts
removing the need for specialisms at the guest OS & application layers
eliminate the vm mobility clock sync ‘hit’
enable vm mobility at any time for resource optimization and DR/BCM
Virtual on-premises environments – private cloud
Strategic wish list
Notes: Drive to normalise precision time services to reduce overall cost and risks
– mainstream precision time services in private and public cloud.
Reduce variation -Dr Edwards Deming stated increased variation can lead to increased cost
Additional thoughts (extra time):
Compare to other DC resource and Moore’s Law
(doubling transistors in CPU every 2 years, mapped to wider computer resources & performance)
Moore’s Law has applied to CPU, memory & storage - over 50 years
- and network bandwidth to extent
Time services performance in general purpose DC have plateaued typically >100mS non-assured through NTP for ~ 20 years.