## Slide 1: Virgin Media’s Synch Journey Evolving to Synch as a Service Wednesday 3rd November

## Slide 2: Virgin Media-O2
Recent joint venture between O2 and Virgin Media
Main synergy in backhaul over VM Network rather than relying on 3rd parties
Necessitates reliable and precise Frequency and Phase Synchronisation
Giving VM the opportunity to refresh their creeking synchronisation distribution infrastructure
Providing synchronisation services to end customers, not just internally

## Slide 3: The Virgin Media Network
Extensive fibre infrastructure down to the last mile serving both residential and business customer
Broadband services based on DOCSIS gradually migrating to XGS-PON facilitated by 40,000 fibre nodes
ROADM based core Optical Network
Packet Optical Metro underpinned by extensive ROADM infrastructure
Core IP/MPLS Network across 40 core sites
High Capacity Uncontended Ethernet Core supporting High Capacity Services
And a legacy TDM infrastructure spanning the whole
IP/MPLS Core
NHCS Core
Metro
Packet Optical
Access
DOCSIS & XGS-PON
Optical Core

## Slide 4: Synchronisation in the current VM Network
Caesium PRTC supporting distribution of frequency synchronisation over the legacy SDH Networks
A mix of new and legacy SSU’s at most core sites
In need of a big refresh and TDM still required as customers are migrated from TDM based voice services to IP
Recent introduction of RPHY to support DOCSIS3.1 residential broadband services drove initial deployment of PTP based phase synchronisation based on the G.8275.2 profile
    Not ideal for future requirements due to location of PRTC/T-GMC and reliance of IP/MPLS Core for transport
    Okay for RPHY as requirements aren’t as strict as other applications (TE of up to 0.5ms)
Merger with O2 and requirement to provide Mobile Backhaul for 4G/5G services has driven a significant shift in our synchronisation strategy and given it the focus that has, in the past, been lacking
    G.8262.1, G.8265.1, G.8275.1 and G.8275.2 profiles all required
    TE requirement of 1µs between T-GMC and Cell Site
    Will absorb RPHY requirement and existing deployment
    Will replace legacy TDM based distribution infrastructure
    Will be used to provide synchronisation to end customers

## Slide 5: The Converged Interconnect Network (CIN)
New high capacity packet optical metro infrastructure
Supporting Ethernet and IP connectivity requirements up to 100Gbit/s:
  Connecting XGS-PON OLT’s, DOCSIS RPHY nodes, Business to Business services, and Mobile Backhaul
  To their Service Definition Platforms in the Core
Integrated coherent optics operating at 100G, 200G and 400G
Connected over Flex-grid Based optical infrastructure
SyncE and integrated T-BC Class C function
Ethernet based with plans to migrate to Segment Routed based MPLS over the medium to long term
Core
Metro
Access

## Slide 6: Mobile Backhaul
Cell Sites connected to CIN nodes at Hub Sites and in some cases street cabinets via 10Gbit/s direct fibre
VRF-Lite based IP solution to allow inter-cell site communications, future front-haul and edge-compute
Crescent based architecture providing end-to-end resilience

## Slide 7: Synchronisation Distribution
Distributed T-GMC’s at all core sites serving CIN domains, at the core edge to ensure TE less than 1µs
Caesium based ePRTC at two backbone sites providing back-up for T-GMC’s
G.8275.1 full-on path support between ePRTC and T-GMC’s
  NHCS Core Elements support SyncE and integrated T-BC Class C function
CIN devices connecting Cell sites and RPD’s have sight of two geographically diverse T-GMC’s using BMCA
  G.8262.1: Physical layer (MBH/RAN and TDM SDH islands)
  G.8265.1: IP unicast facilitated by dedicated VRF instances on CIN (MBH/legacy RAN)
  G.8275.1: Ethernet multi-cast (MBH/RAN)
  G.8275.2: IP unicast facilitated by dedicated VRF instances (RPHY/DOCSIS)
IP/MPLS Core
NHCS Core
Metro
Packet Optical
Access
DOCSIS & XGS-PON
Optical Core

## Slide 8: Overcoming the Challenges of Synch Distribution
A number of inherent challenges within a modern network must be considered and overcome, especially to achieve a Time Error of 1µs:
  Fibre Asymmetry: All bi-directional fibre connectivity is within the same cable and intra-site connectivity will follow tight guidelines to negate any asymmetry.
  Dispersion Compensation: No dispersion compensation on the core or on new metro infrastructure; Bragg gratings mostly deployed on legacy.
  Coherent Optics: TE is manageable within the deployed design to achieve current requirements.
  OTN Mapping: No OTN switching is deployed in the network and the minimal OTN mapping that we use has manageable TE characteristic.
  Photonic Components: ROADM’s, Amps and Filters are designed to meet stringent synchronisation requirements.
  IP Routing & Switching: All routers and switches within the distribution infrastructure will meet T-BC Class C requirements.
A distributed T-GMC is used to achieve TE requirements, the T-GMC’s being deployed at the Core/Metro Boundary
Use of the Ethernet based, synch aware, high capacity core infrastructure rather than the Core IP/MPLS infrastructure
Deployment of an Optical Timing Channel on new coherent-only metro infrastructure

## Slide 9: Delivering the Synchronisation Services
T-GMC at core sites delivers synchronisation (all required profiles) into the CIN infrastructure
Synchronisation of legacy SDH also delivered from T-GMCs on traditional 2Mbit/s / 2MHz feeds (may required expansion shelves to provide volumes of ports)
End services take required synchronisation profiles from the CIN devices:
  Remote PHY RPDs and Cell Site Gateway (mobile RAN) connected via CIN (10GE)
  Synchronisation would be integral to any Ethernet based connectivity services
  Compact NTU device to provide specific synchronisation (only) service, connected to CIN to derive the timing information
Customer Premises
VM Access Hub Site
Metro/Access SDH
VM Access Hub Site
VM Access Hub Site
VM Core Site
VM Core Site
8180
8180
5170
5170
T
-
BC
T
-
BC
T
-
BC
T
-
BC
T
-
BC
T
-
BC
T
-
BC
T
-
BC
ITU
-
T G.8275.1
Full on
-
path support
Primary PTP Ethernet Stream
Primary PTP Ethernet Stream
Secondary PTP Ethernet Stream
Synchronous Ethernet
T
-
BC
T
-
BC
CSG
5171
5171
8180
8180
5171
5171
Synchronous Ethernet
Synchronous Ethernet
Synchronous Ethernet
5171
5171
Secondary PTP Ethernet Stream
5170
5170
TDM Switch
Optional Expansion shelf or SSU
From ePRTC
From ePRTC
Metro/Access SDH
Metro/Access SDH
E1
E1
E1
E1
RPD
SaaS
PTP, NTP, BITS, SyncE, ToD, etc.
Compact T-BC/GMC
1GE
Customer Premises
NTU
1GE/10GE
T-BC
10GE