## Slide 1: Time Card - Democratize Time Appliances
Ahmad Byagowi (OCP-TAP)

## Slide 2
Open Compute Project Time Appliance Project (TAP)
https://www.opencompute.org/wiki/Time_Appliances_Project (www.ocptap.com)
Mission:
Work Streams:

## Slide 3
T2
T4
T3
T4
T3
T2
T2
Accuracy vs Precision in Sync
T1
UTC
T4
T1
T3
UTC
T1
UTC
UTC
T1
T2
T3
T4
Not Accurate
Not Precise
Accurate
Not Precise
Not Accurate
Precise
Accurate
Precise
Like NTP
No Sync
Like PTP
Like PTP + Time Card

## Slide 4: Open Time Server
https://engineering.fb.com/2016/02/18/core-data/netnorad-troubleshooting-networks-via-end-to-end-probing/
GNSS Receiver
High Stability Oscillator
PPS
PPS
ToD
Discipline
NIC with PPS out (and/or) in
PCIe
Time Card
Clock Processing FPGA
Host CPU
PCIe
Antenna
Time Card

## Slide 5: Time Card
https://engineering.fb.com/2016/02/18/core-data/netnorad-troubleshooting-networks-via-end-to-end-probing/
GNSS Receiver
High Stability Oscillator
PPS
PPS
ToD
Discipline
PCIe
Time Card
Clock Processing FPGA
Antenna

## Slide 6: Time Card
https://engineering.fb.com/2016/02/18/core-data/netnorad-troubleshooting-networks-via-end-to-end-probing/
GNSS Receiver
High Stability Oscillator
PPS
PPS
ToD
Discipline
PCIe
Time Card
Clock Processing FPGA
Antenna
Advanced “GPSDO”
Interface

## Slide 7: Advanced “GPSDO”
https://engineering.fb.com/2016/02/18/core-data/netnorad-troubleshooting-networks-via-end-to-end-probing/
GNSS Receiver1
High Stability Oscillator
PPS MAC
PPS1
ToD1
Discipline
Clock Processing FPGA
L1/L2
GNSS Receiver2
PPS2
ToD2
L1/L5
PPS1
PPS2
Optional

## Slide 8: FPGA
https://engineering.fb.com/2016/02/18/core-data/netnorad-troubleshooting-networks-via-end-to-end-probing/

## Slide 9: Interface
https://engineering.fb.com/2016/02/18/core-data/netnorad-troubleshooting-networks-via-end-to-end-probing/
PCIe
  PCIe x1 (18 pins) generation 1.0 or above on a x4 form-factor
  Generic, supporting multiple OS versions
  Exposes PHC device in Linux (/dev/ptpX) as well as PPS (/dev/ppsY)
  Exposes leap second indicator to a shared memory segment read by chrony/ptp4l
1PPS / 10MHz SMA output
1PPS / 10MHz SMA input
IRIG-B input output
DCF77 input output
# ls -l /sys/class/timecard/ocp0/
total 0
-r--r--r--. 1 root root 4096 Oct 21 05:24 available_clock_sources
-r--r--r--. 1 root root 4096 Oct 21 05:24 available_sma_inputs
-r--r--r--. 1 root root 4096 Oct 21 05:24 available_sma_outputs
-rw-r--r--. 1 root root 4096 Oct 21 05:24 clock_source
lrwxrwxrwx. 1 root root 0 Oct 21 05:24 device -> ../../../0000:15:00.0
-rw-r--r--. 1 root root 4096 Oct 21 05:24 external_pps_cable_delay
-r--r--r--. 1 root root 4096 Oct 21 05:24 gnss_sync
lrwxrwxrwx. 1 root root 0 Oct 21 05:24 i2c -> ../../xiic-i2c.5376/i2c-0
-rw-r--r--. 1 root root 4096 Oct 21 05:24 internal_pps_cable_delay
-rw-r--r--. 1 root root 4096 Oct 21 05:24 irig_b_mode
drwxr-xr-x. 2 root root 0 Oct 21 05:24 power
lrwxrwxrwx. 1 root root 0 Oct 21 05:24 pps -> ../../../../../virtual/pps/pps6
lrwxrwxrwx. 1 root root 0 Oct 21 05:24 ptp -> ../../ptp/ptp12
-r--r--r--. 1 root root 4096 Oct 21 05:24 serialnum
-rw-r--r--. 1 root root 4096 Oct 21 05:24 sma1
-rw-r--r--. 1 root root 4096 Oct 21 05:24 sma2
-rw-r--r--. 1 root root 4096 Oct 21 05:24 sma3
-rw-r--r--. 1 root root 4096 Oct 21 05:24 sma4
lrwxrwxrwx. 1 root root 0 Oct 21 05:24 subsystem -> ../../../../../../class/timecard
-rw-r--r--. 1 root root 4096 Oct 21 05:24 ts_window_adjust
lrwxrwxrwx. 1 root root 0 Oct 21 05:24 ttyGNSS -> ../../tty/ttyS4
lrwxrwxrwx. 1 root root 0 Oct 21 05:24 ttyGNSS2 -> ../../tty/ttyS5
lrwxrwxrwx. 1 root root 0 Oct 21 05:24 ttyMAC -> ../../tty/ttyS6
lrwxrwxrwx. 1 root root 0 Oct 21 05:24 ttyNMEA -> ../../tty/ttyS7
-rw-r--r--. 1 root root 4096 Oct 21 05:23 uevent
-rw-r--r--. 1 root root 4096 Oct 21 05:24 utc_tai_offset
Driver is included in the mainstream Linux Kernel
Initial primitive version (5.2)
Exposing all devices version (5.15)

## Slide 10: How to use it
https://engineering.fb.com/2016/02/18/core-data/netnorad-troubleshooting-networks-via-end-to-end-probing/
For PTP Time Server (Grandmaster)
Via PCIe (PHC2SYS)
Via PPS (TS2PHC)
Via Reverse PPS (in progress)
For Camera and Audio Systems
IRIG-B
PPS
For NTP Time Server
Via PCIe (Chrony)
Other Applications
Bipolar and Multi Channel TDC (Multiple PPS in)
Over PCIe Event Time Stamping

## Slide 11: Performance
https://engineering.fb.com/2016/02/18/core-data/netnorad-troubleshooting-networks-via-end-to-end-probing/
Time Card
NIC
NIC
PPS out
PPS in
PPS out
C
PTP over ethernet
PPS out
D

## Slide 12: Performance
https://engineering.fb.com/2016/02/18/core-data/netnorad-troubleshooting-networks-via-end-to-end-probing/

## Slide 13: Performance
https://engineering.fb.com/2016/02/18/core-data/netnorad-troubleshooting-networks-via-end-to-end-probing/

## Slide 14: Previous Versions
December 2020
March 2021
April 2021
July 2021
February 2021
October 2020
Sep 2020
November 2020

## Slide 15: Latest Versions
Dual GNSS with Rb Clock (SA.53)
Low Power with Cs Clock (SA.45s)
Can be found on www.timingcard.com

## Slide 16: Acknowledgment

## Slide 17: Thank You