## Slide 1
An Assessment of the Resilience of Multi-Constellation Multi-Frequency (MCMF) GNSS Receivers to Radio Frequency Interference (RFI)
Akis Drosinos, Guy Buesnel, Mark Hunter
Spirent Communications

## Slide 2: GNSS Vulnerabilities
Chart: 1 PPS Vs Time Vs RFI power level
Figure 1: Commercial Timing Receiver (GPS L1/L2) with no Resilience

## Slide 3
The recently published DHS Resilient PNT Conformance Framework (Version 1.0) contains definitions of four (five if level zero is counted - no resilience at all) levels of resilience for PNT.
  The levels should be selected based on the users’ risk tolerance, budget and application criticality (Homeland Security 2021).
The framework is PNT source agnostic, outcome based and is intended to apply to all User Equipment (UE) that outputs PNT solutions, including PNT systems of systems, integrated PNT receivers and PNT source components, such as GNSS chipsets (Homeland Security 2021).
Resilience, as defined in (Homeland Security 2021), is “the ability to prepare for and adapt to changing conditions and withstand and recover rapidly from disruptions”.
Resilient PNT Conformance Framework V1.0 (1/2)

## Slide 4
Resilient PNT Conformance Framework V1.0 (2/2)
Key concepts of the Framework
Defence in depth
    Resilience should be designed and incorporated throughout the entire processing chain and system.
    Diversity of both PNT sources and resilience mechanisms will increase the robustness of the implementation.
Core functions
P
RS
RC
Resilience levels
(P)
(RS, RC)
(RC)
(P, RS)
(RS, RC)

## Slide 5
10 MHz out
1 PPS out
1 PPS in
10 MHz in
GSS8366 ICU
High RF out
ICU signal in
RFI out
ICU RFI combiner
switch
Remote
DUT
Combined RF out
Meas. 1 PPS out
Rubidium 10 MHZ
laptop
Meas. 1 PPS in
Serial connection
ETH cable
ISG
Figure 2: RFI Test set-up
GSS7000
Paragon-X

## Slide 6
GNSS RFI test parameters
Test Parameters (CW Swept jammer) | 
Interferer initial RF power (dBm) | -98.5
Frequency range (MHz) | GPS L1 (1570.42 - 1580.42) GAL E5b (1202.14 - 1212.14)
Number of points | 10
Dwell Time (ms) | 100
Table 1: Test parameters

## Slide 7
Resilience Level 1 test set-up
DUT was set to use GAL E1 and GPS L1 signals.
GPS L1 band had increasing RFI power (10 MHz swept CW) gradually applied until DUT entered holdover mode. Then, the threat was removed and the DUT was rebooted.
During the run, the DUT had to:
  Verify that the data from the external input was valid and output valid 1 PPS (P).
  Support full system recovery and return to the expected performance after the removal of the threat (RS, RC).
Pass / Fail criteria:
  Pass: The DUT is reset and able to recover fully.
  Fail: The DUT is reset, but never recovers.
1 hour
Scenario time into run
1 hour
5 dB/5 min
Warm up
RFI off
RFI on
RFI off
Figure 3: Resilience Tests 1 & 2 schematic
1/2 hour
-53.5 dBm
Single-band Primary Reference Time Clock (PRTC)
Recovery
3.5 hours
P
RS
RC

## Slide 8
Resilience Level 1 test results
Chart: 1 PPS TE Vs RFI over time
Threat removed / DUT rebooted
1 PPS lost
Prevent
Full recovery
Respond
Holdover state at -68.5 dBm
Figure 4: Single-band PRTC, jammed on GPS L1, compliant with Resilience Level 1

## Slide 9
Resilience Level 2 test set-up
The DUT was configured to use GAL E1, E5b and GPS L1 signals.
GPS L1 had increasing RFI power gradually applied to cause the DUT to switch to the E5b band and continue to output valid 1 PPS measurements. Then, the threat was removed in order for it to recover fully.
GAL E5 had increasing RFI power gradually applied in order for the DUT to reject GAL E5b signals and continue using only GPS L1 and GAL E1 signals. Then, the threat was removed in order for it to recover fully.
During the run, the DUT had to:
  Identify compromised PNT sources and prevent them from contributing to erroneous PNT solutions (P, RS).
  Continue providing a PNT solution in the presence of the threat, while responding to it.
  Support automatic recovery of individual PNT sources without disrupting the PNT output (RS, RC).
Pass / Fail criteria:
  Pass: The PRTC does not enter into holdover mode and continues to provide a valid solution.
  Fail: The PRTC does enter into holdover mode due to not being able to switch to the E5b band.
Multi-band Primary Reference Time Clock (PRTC)
P
RS
RC

## Slide 10
Resilience Level 2 test results
Figure 5: Multi-band PRTC, jammed on GPS L1, partially compliant with Resilience Level 2
Chart: 1 PPS TE Vs RFI over time
Holdover state at -53.5 dBm
Exited Holdover state
Threat removed
Prevent
Full recovery
Respond
PRTC-B limit
PRTC-B limit
1 PPS TE | Column1 | Values (ns)
Pre RFI | Mean | -5.553581344
 | Max | -3
 | Min | -9
 | Stdn | 0.963523453
Post RFI | Mean | -5.163759145
 | Max | 8
 | Min | -29
 | Stdn | 6.367120179
Table 2: 1 PPS TE values

## Slide 11
Resilience Level 2 test results
Chart: 1 PPS TE Vs RFI over time
Figure 6: Multi-band PRTC, jammed on GAL E5, compliant with Resilience Level 2
PRTC-B limit
PRTC-B limit
Threat removed
Prevent
Respond
GAL E5 not part of the solution any more
Full recovery
GAL E5 part of the solution again
1 PPS TE | Column1 | Values (ns)
Pre RFI | Mean | -5.58856191
 | Max | -3
 | Min | -9
 | Stdn | 0.98829943
Post RFI | Mean | -4.969611705
 | Max | 14
 | Min | -20
 | Stdn | 6.70541389
Table 3: 1 PPS TE values

## Slide 12
Comments / Suggestions
The resilience levels presented here depend on the specific scenario that was used, i.e. swept CW Jammer.
We cannot conclude if the multi-band PRTC was compliant with the Resilience Level 2. This is due to the lack of knowledge of the internal workings of the DUT (L1 vs E5).
It is crucial to understand your system in fine detail. Testing in a controlled environment is vital.
Manually resetting a GNSS receiver (requirement of Resilience Level 1) can be problematic if RFI is present.
Further work required to define use cases to complement/reinforce the Conformance Framework.

## Slide 13: References
Homeland Security (2021), Resilient PNT Conformance Framework Report. Viewed 20 Aug 2021. URL: https://www.dhs.gov/publication/st-resilient-pnt-conformance-framework#